## Slide 1: 405 Project Group 3
Murtada Al Hasan
Khaled Al Badeea
Mohammed Al Sulayyim
Mohammed Al Ghamdi

## Slide 2: Content 01 Scope The Problem Objectives System Description Initial Assumptions Input Data Analysis 02 03 04 05 06
An Introduction to the Project
What we are trying to achieve
What is the wideness of the project
Breif Explanation of the system
Data Assumptions, Structural Assumptions and Logical Assumptions
How did we analyised and obtained the data

## Slide 3: Content 07 Output Analysis Arena Model Validation Scenarios Recommendations 08 09 10 11
Simulation Model that representa the real system
Making sure that the model has the same behavior of the real system
Making sure that the output is logical and the number of replications are enough
Improving the real life system by conduction several tests on the model
Based on the Output analysis and the scenarios

## Slide 4: MISSION STATEMENT The Problem
A new Concept!!
Tiny Fields

## Slide 5: The Problem
Aramco Production
Shayba Field Production
Our Tiny Field Production

## Slide 6: The Problem
1
2
3
Blending
Distillation
Cracking
1
2
3

## Slide 7: Objectives
Too Expensive!!
Applying several scenarios in the model instead
Maximize the Company Profit
Testing the efficiency of the new concept

## Slide 8: Scope of The Project
These days, oil and its derivatives are one of the most important things. Many products are depending on the oil.
Oil companies always want to find new profitable oilfields, with a large amount of oil.
However, some oilfields are not profitable and might have unwanted consequences.
If an oil company wants to check if a new oilfield will be profitable, simulation is an efficient tool to test and check a model for many scenarios before building it physically.

## Slide 9: System Description Distillation The system consists of three main steps Cracking Blending
1
2
3

## Slide 10: Distillation
Distillation has three subparts:
  distillation column.
  Condenser.
  reflux drum.
The oil that is extracted is a mixture of many components and need to be separated.
The crude oil separated based on:
Volatility.
the boiling point. (up to 600 degrees Celsius)
The mixture boiled and forms gases that will go to the vapor phase with the lowest boiling point.
The liquid and solid parts will be separated according to their boiling points.
The liquid will go to the condensers.
In the condensers, the liquid will be cooled again the be transported either to the cracker or directly to the blender through the reflux drum by a specified ratio of crude oil.

## Slide 11: Cracking
The crude oil most be liquid by breaking the carbon-carbon bonds by heating them in high temperature (around 816o C) and throw away the solids that cannot be transformed to liquids.

## Slide 12: Blending
In the blending step, we have three different products from each process (distillation and cracking) with the same ON (82 or 98) but different in price.
In blending step, we need to have finally three types of ON with the lowest price (87, 89, 92), by combining two products from each previous step to have the final three products.

## Slide 13: Initial Assumptions: 01 Each truck can carry 190 bbl. FIFO Crude oil is arrived by trucks. The whole amount of crude oil that is arrived by a single truck is considered as one entity. Xij is divided instantaneously during the processes. 02 03 04 05
The system services the entities that come first.

## Slide 14: Initial Assumptions: 06 The cracking process is done by a single step. The initial distribution of the crude oil The distribution of a processing time Tiny field 07 08 09
is equal for each one of blends through the three sequences (33.33% for each).
can be divided into partial sub-processes times, where the summation of the distribution parameters in the sub-processes is equal to the parameters in the main process.
This simulation model for the tiny field is general and applicable for any other tiny fields (e.g. 20 tiny fields can be built instead of normal field with the same simulated model to minimize the risk of building the huge field).

## Slide 15: INPUT DATA AND ITS ANALYSIS IA

## Slide 16: DATA TYPE 01 Arrival Time Cracking Time Distillation Time Blending Time 03 02 04
Assumed to be exponential
Known to be random
Possible Data
Assumed to be random

## Slide 17: MISSION STATEMENT Arrival Time EXPO( 2.5 )
It was determined by logical calculations
Aim
Utilize the capacity as much as we can
(40,000 bbl)

## Slide 18: MISSION STATEMENT Distillation Time UNIF(1.56,2.32)
It was determined by knowing that distillation can take around
4 to 6 hours
Estimation
Distillation time is 153 times less
Divided into smaller processes

## Slide 19: MISSION STATEMENT Cracking Time EXPO( 1.33 )
Known to be completely random, and it is around
3.4 hours
Recall
our tiny field we simulated is
(153 times) less than usual field

## Slide 20: MISSION STATEMENT Blending Time EXPO( 0.55 )
Including the transfer time
TT = 0.05
So
The blending time in a single stream

## Slide 21: ARENA MODEL The model is built carefully, covering the whole process of Distillation, Cracking, and Blending AR

## Slide 22: ARENA MODEL

## Slide 23: Validation V

## Slide 24: Validation 01 High Face Validity Model Assumption Validation 02
By an expert
Sensitivity Analysis
Data Assumptions
Structural Assumptions

## Slide 25: MISSION STATEMENT High Face Validity
By an expert
We asked Dr. Rahul N. Gajbhiye
An expert in the downstream of the crude oil refinery which we are simulating (downstream includes Distillation, cracking and blending).
Assistant Professor in the College of Petroleum Engineering and Geosciences at KFUPM

## Slide 26: MISSION STATEMENT High Face Validity
Sensitivity Analysis
To have Logical results that matches with real life crude oil system
Decreasing ratio of reflux | Increasing waiting time | Increasing queue length
Increasing ratio of distillation | Decreasing the total time | Decreasing # of units out
Decreasing ration of pre-cracking | Decreasing the utilization | Increasing the # of units out
Increasing blending time | Increasing the utilization | Increasing the total time

## Slide 27: MISSION STATEMENT Model Assumption Validation
Structural Assumptions
Chart: FIFO vs Priority
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Served FIFO | 24 | 48 | 72 | 96 | 120 | 144 | 168 | 192
Served by priority | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001

## Slide 28: MISSION STATEMENT Model Assumption Validation
Structural Assumptions
Chart: Comparing no consideration time vs various consideration times of Xij dividing
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
No consideration | 24 | 48 | 72 | 96 | 120 | 144 | 168 | 192
10 mins consideration | 20 | 44 | 68 | 92 | 116 | 140 | 164 | 188
25 mins Consideration | 14 | 38 | 62 | 86 | 110 | 134 | 158 | 182

## Slide 29: MISSION STATEMENT Model Assumption Validation
Data Assumptions
Distribution | Process | Why?
Uniform | Distillation | Max, and Min values ONLY
Exponential | Trucks arrival time | Common in arrival events
Exponential | Cracking & Blending | Complete of them completely random

## Slide 30: OUTPUT ANALYSIS 0A

## Slide 31: Assumptions
Maximum allowable error of time is 1 min.
The waiting time in the real system is 4.25 min.
The total time in the real system is 6.4 min.
The time in the queue of the distillation unit in the real system is 3.2 min.
Maximum allowable error of the number of oil trucks is 25 trucks.
The number of oil trucks entered in the real system is 1030 trucks.
Maximum allowable error of WIP is 0.45.
The value of WIP in the real system is 2.3.
Maximum allowable error of utilization is 0.075.
The utilization of the distillation unit in the real system is 0.75.
The utilization of the blending machine and cracker in the real system is 0.06.

## Slide 32: OUTPUT ANALYSIS 01 Time is the distillation queue Waiting Time 03 02
Average: 3.82 min
Half width: 0.32
C.I.: (3.50, 4.14)
0.32 < 1
Total Time
Average: 6.12 min
Half width: 0.32
C.I.: (5.8, 6.44)
0.32 < 1
Average: 3.81 min
Half width: 0.32
C.I.: (3.49, 4.13)
0.32 < 1
# of oil trucks entered the system
04
Average: 1053.73
Half width: 13.82
C.I.: (1039.91, 1067.55)
13.82 < 25

## Slide 33: OUTPUT ANALYSIS 05 Utilization: Blending machine WIP Utilization: Cracker 07 06 08
Average: 2.45
Half width: 0.15
C.I.: (2.3, 2.6)
0.15 < 0.45
Utilization: Distillation unit
Average: 0.7881
Half width: 0.01
C.I.: (0.7781, 0.7981)
0.01 < 0.075
Average: 0.0647 *
Half width: ~0.00
~0.00 < 0.075
Actual =
Average: 0.0550 *
Half width: ~0.00
~0.00 < 0.075
Actual =

## Slide 34: MISSION STATEMENT Number of Trucks
Each Truck can carry
190 bll of oil

## Slide 35: Scenarios and Improvements on The System

## Slide 36: System Operations Company Policies
Adjusting the Distribution of the entites before blending
Adjusting the ratio of the entities to be cracked
Adjusting the working times policy
Two Types Of the Scenarios

## Slide 37: Adjusting the Distribution of the entites before blending 01

## Slide 38: Before After
New Distribution is: 10% of (87 ON), 33.33% of (89 ON) and 56.67% (92 ON)
WHY??
The Distribution Initially was 33.33% for each Final Product

## Slide 39: Old Revenue 38,797,506

## Slide 40: 40,529,736 SR
The revenue increased by around 1.7 Million
Conclusion?

## Slide 41: Adjusting the ratio of the entities to be cracked 02

## Slide 42: Before After
75% of the cracker is used
Represents 39.4% of the entities
100% of the cracker capacity uesd
Represents 52.6% of the arrived entities

## Slide 43: Old Revenue 38,797,506 SR

## Slide 44: 42,620,382 SR
The revenue increased by around 3.8 Million
Conclusion?

## Slide 45: Adjusting the working times policy 03

## Slide 46: Before After
The daily Working timea are as follow:
8, 8, 8, 8, 8 hours
The Daily working times are as follow:
4, 12, 12, 12, 4 hours

## Slide 47: Old Revenue 38,797,506

## Slide 48: 35,240,220 SR
The revenue Decreased by around 3.56 Million
But, overtimes hours savings are around 2.64 Million
So the Total Lose is around 0.92 Million
Conclusion?

## Slide 49: Contributions We contributed in:
1- Increasing the annual revenue of the tiny field by adjusting distributing of items that go to the blending sequences
2- Increasing the annual revenue of the tiny field by adjusting the amount of oil that go to the cracking process
3- Supporting the company policy of using the (4 12 12 12 4) working hours system

## Slide 50: RECOMMENDATION R

## Slide 51: Recomendation We Recommend:
Running the simulation model with larger number of replications will give more accurate results.
Using the second system working hours (4 12 12 12 4) will have better net revenue to the company.
The third product (ON 92) have the best revenue, the company should increase it to have better net revenue (with considering other constrains)
Adjusting the ratio of the oil that comes from the distillation tower to the cracker will gives a better revenue to the company.